## Slide 1: Factors affecting leg- length at various levels, including the knee
Multitom Rax True2scale Body Scan1 clinical case Orthopedic Hospital Schloss Werneck, Germany
1 Option
StudyID: 5aag676

## Slide 2: Background Total hip arthroplasty (THA)
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. | 1 THA: total hip arthroplasty
Gold-Standard procedure to plan THA1
X-ray image acquisition: Pelvis overview
      Lying or weight-bearing (optimal)
      Acquired in a.P. or including a second view lat.
Disadvantages
      Only indirect measurement of leg-length possible (true length only measurable with whole leg image)
      If additional CT acquisition is done (i.e., for 3D preoperative planning), patient is not in weight-bearing position
Measurements to plan THA (incl. resulting leg-length)
      Reference line within the pelvis, e.g., at the pelvic teardrop
      Parallel to the reference line, a second line is placed at the femoral bone, e.g., at the greater trochanter
      If the parallel line does not align with both reference points, the parallel difference is set equal to the leg-length discrepancy
1
2
3
1
2
3

## Slide 3: Clinical background
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed.
Patient
Sex Female
BMI 16.3 kg/m²
Already treated with a left total knee endoprosthesis. The right knee also shows advanced, but so far painless, degeneration. Presentation with bilateral coxarthrosis (left more than right). At that time, following conventional planning, a left total hip endoprosthesis was implanted. The patient now presents again for implantation on the opposite side.
Anamnesis
StudyID: 5aag677
Year of birth 1963

## Slide 4: Clinical background and indication for Multitom Rax True2scale Body Scan1
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. | 1 Option
Patient
Already treated with a left total knee endoprosthesis. The right knee also shows advanced, but so far painless, degeneration. Presentation with bilateral coxarthrosis (left more than right). At that time, following conventional planning, a left total hip endoprosthesis was implanted. The patient now presents again for implantation on the opposite side.
Indication for True2scale Body Scan1 Left side: Fully implanted lower extremity, right side: still in its original condition. The necessity of True2scale Body Scan1 to include all levels in the planning of leg length, especially in cases of pathologies or different states of reconstruction at various levels.
Anamnesis
Sex Female
BMI 16.3 kg/m²
Year of birth 1963

## Slide 5: Multitom Rax True2scale Body Scan1 Differences Pelvis Overview vs. T2S1
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. | 1 Option
Gold-standard
Pelvis overview
2 mm
Leg-length discrepancy | 2 mm
Tube voltage | 81 kV
Current time product | 14.4 mAs
Dose area product | 54.7 µGym²
StudyID: 5aag677
Leg-length discrepancy | 2 mm
Scan range | 86.6 cm
Scan time | 10.8 sec
Tube voltage | 81 kV
Current time product | 54 mAs
Dose area product | 9.2 µGym²
True2scale Body Scan1
a.p. using upright S protocol
StudyID: 5aag676
2 mm

## Slide 6: Multitom Rax True2scale Body Scan1 Diagnostic Findings & Results
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. | 1 Option
Results
StudyID: 5aag675
StudyID: 5aag676
Post-surgery
Pre-surgery
True2scale Body Scan1 revealed a 2 mm leg-length discrepancy.
Follow-up scan after revision
Uncomplicated implantation with almost equal leg length, with a 6 mm discrepancy on the left side. This leaves some space for the treatment of the left knee in the further course.

## Slide 7
1 The statements by Siemens Healthineers customers described herein are based on results that were achieved in the customer’s unique setting. Since there is no “typical” hospital and many variables exist (e.g., hospital size, case mix, level of IT adoption) there can be no guarantee that other customers will achieve the same results.
“The T2S scan provides us with a seamless and distortion-free overview across many levels.” 1
Manuel Scholl, MD Orthopedic Hospital Schloss Werneck, Germany

## Slide 8
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. True2scale Body Scan is an option.
Results from case studies are not predictive of results in other cases. Results in other cases may vary.
Manuel Scholl is employed by an institution that receives financial support from Siemens Healthineers for collaborations.