## Slide 1: Blurred anatomical landmarks
Multitom Rax True2scale Body Scan1 clinical case Orthopedic Hospital Schloss Werneck, Germany
1 Option
StudyID: 5aag664

## Slide 2: Background Total hip arthroplasty (THA)
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. | 1 THA: total hip arthroplasty
Gold-Standard procedure to plan THA1
X-ray image acquisition: Pelvis overview
      Lying or weight-bearing (optimal)
      Acquired in a.P. or including a second view lat.
Disadvantages
      Only indirect measurement of leg length possible (true length only measurable with whole leg image)
      If additional CT acquisition is done (i.e., for 3D preoperative planning), patient is not in weight-bearing position
Measurements to plan THA (incl. resulting leg-length)
      Reference line within the pelvis, e.g., at the pelvic teardrop
      Parallel to the reference line, a second line is placed at the femoral bone, e.g., at the greater trochanter
      If the parallel line does not align with both reference points, the parallel difference is set equal to the leg-length discrepancy
1
2
3
1
2
3

## Slide 3: Clinical background
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed.
Patient
Sex Male
BMI 26.3 kg/m²
Status post corrective osteotomy in 1981 with a leg-length discrepancy of 1 cm. The patient experiences significant suffering and severe restriction of movement.
On the pelvis overview, the anatomical landmarks are markedly blurred, resulting in reduced planning accuracy due to the difficulty in identifying them.
Anamnesis
StudyID: 5aag666
Year of birth 1967

## Slide 4: Clinical background and indication for Multitom Rax True2scale Body Scan1
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. | 1 Option
Patient
Status post corrective osteotomy in 1981 with a leg-length discrepancy of 1 cm. The patient experiences significant suffering and severe restriction of movement.
On the pelvis overview, the anatomical landmarks are markedly blurred, resulting in reduced planning accuracy due to the difficulty in identifying them.
Indication for True2scale Body Scan1 Use of True2scale Body Scan1 to reduce planning inaccuracies.
Anamnesis
Sex Male
BMI 26.3 kg/m²
Year of birth 1967

## Slide 5: Multitom Rax True2scale Body Scan1 Differences Pelvis Overview vs. T2S1
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. | 1 Option
Gold-standard
Pelvis overview
11 mm
Leg-length discrepancy | 11 mm
Tube voltage | 90 kV
Current time product | 12 mAs
Dose area product | 158.2 µGym²
StudyID: 5aag666
Leg-length discrepancy | 15 mm
Scan range | 104.2 cm
Scan time | 13.1 sec
Tube voltage | 81 kV
Current time product | 497 mAs
Dose area product | 97.4 µGym²
True2scale Body Scan1
a.p. using upright L protocol
StudyID: 5aag664
15 mm

## Slide 6: Multitom Rax True2scale Body Scan1 Diagnostic Findings & Results
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. | 1 Option
Results
True2scale Body Scan1 reveals that the previously assumed leg-length discrepancy is greater than 11 mm (15 mm)
Follow-up scan after revision
Uncomplicated surgical course with equalized leg length postoperatively (less than 5 mm difference).
StudyID: 5aag665
StudyID: 5aag664
Post-surgery
Pre-surgery
      Revision surgery

## Slide 7
1 The statements by Siemens Healthineers customers described herein are based on results that were achieved in the customer’s unique setting. Since there is no “typical” hospital and many variables exist (e.g., hospital size, case mix, level of IT adoption) there can be no guarantee that other customers will achieve the same results.
“The T2S scan provides planning confidence in complex anatomical situations by offering a good overall view.”1
Manuel Scholl, MD Orthopedic Hospital Schloss Werneck, Germany

## Slide 8
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. True2scale Body Scan is an option.
Results from case studies are not predictive of results in other cases. Results in other cases may vary.
Manuel Scholl is employed by an institution that receives financial support from Siemens Healthineers for collaborations.