## Slide 1: Restricted view of overall anatomy
Multitom Rax True2scale Body Scan1 clinical case Orthopedic Hospital Schloss Werneck, Germany
1 Option
StudyID: 5aag667

## Slide 2: Background Total hip arthroplasty (THA)
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. | 1 THA: total hip arthroplasty
Gold-Standard procedure to plan THA1
X-ray image acquisition: Pelvis overview
      Lying or weight-bearing (optimal)
      Acquired in a.P. Or including a second view lat.
Disadvantages
      Only indirect measurement of leg length possible (true length only measurable with whole leg image)
      If additional CT acquisition is done (i.e., for 3D preoperative planning), patient is not in weight-bearing position
Measurements to plan THA (incl. resulting leg-length)
      Reference line within the pelvis, e.g., at the pelvic teardrop
      Parallel to the reference line, a second line is placed at the femoral bone, e.g., at the greater trochanter
      If the parallel line does not align with both reference points, the parallel difference is set equal to the leg-length discrepancy
1
2
3
1
2
3

## Slide 3: Clinical background
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. | 1 THA: total hip arthroplasty
Patient
Sex Male
BMI 44.1 kg/m²
Status post a traffic accident in 1983 with a screwed acetabular fracture, severe bilateral coxarthrosis, leg-length discrepancy, and pronounced flexion contracture of the right hip with a forward-bent upper body. Tape measure suggests a leg-length discrepancy of 3 cm.
The cause of the leg-length discrepancy cannot be definitively assigned to one side due to the degree of destruction of both hips.
Anamnesis
StudyID: 5aag668
Year of birth 1948

## Slide 4: Clinical background and indication for Multitom Rax True2scale Body Scan1
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. | 1 Option
Patient
Status post a traffic accident in 1983 with a screwed acetabular fracture, severe bilateral coxarthrosis, leg-length discrepancy, and pronounced flexion contracture of the right hip with a forward-bent upper body.
The cause of the leg-length discrepancy cannot be definitively assigned to one side due to the degree of destruction of both hips.
Indication for True2scale Body Scan1 Use of True2scale Body Scan1 to plan surgery and identify the correct side causing the leg-length discrepancy.
Anamnesis
Sex Male
BMI 44.1 kg/m²
Year of birth 1948

## Slide 5: Multitom Rax True2scale Body Scan1 Differences Pelvis Overview vs. T2S1
4 mm
?
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. | 1 Option
Gold-standard
Pelvis overview
Leg-length discrepancy | 4(?) mm
Tube voltage | 112.7 kV
Current time product | 59 mAs
Dose area product | 161.4 µGym²
StudyID: 5aag668
Leg-length discrepancy | 8 mm
Scan range | 101.8 cm
Scan time | 12.7 sec
Tube voltage | 81 kV
Current time product | 429 mAs
Dose area product | 89.7 µGym²
True2scale Body Scan1
a.p. using upright XL protocol
8 mm
StudyID: 5aag667

## Slide 6: Multitom Rax True2scale Body Scan1 Diagnostic Findings & Results
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. | 1 Option
Results
True2scale Body Scan1 reveals that, surprisingly, only a small anatomical leg-length discrepancy of about 8 mm is observed, whereas previously 3 cm had been measured with a tape measure. Additionally, the knee joints were found to be at different heights. Therefore, the cause of the leg-length discrepancy is functional and not anatomical.
Follow-up scan after revision
Uncomplicated surgical course with equalization of leg-length postoperatively (less than 5 mm difference).
StudyID: 5aag669
StudyID: 5aag667
Post-surgery
Pre-surgery

## Slide 7
1 The statements by Siemens Healthineers customers described herein are based on results that were achieved in the customer’s unique setting. Since there is no “typical” hospital and many variables exist (e.g. hospital size, case mix, level of IT adoption) there can be no guarantee that other customers will achieve the same results.
“The T2S scan can help to distinguish functional from anatomical deficits.”1
Manuel Scholl, MD Orthopedic Hospital Schloss Werneck, Germany

## Slide 8
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. True2scale Body Scan is an option.
Results from case studies are not predictive of results in other cases. Results in other cases may vary.
Manuel Scholl is employed by an institution that receives financial support from Siemens Healthineers for collaborations.