## Slide 1: Identifying the causes of leg-length discrepancy
Multitom Rax True2scale Body Scan1 clinical case Orthopedic Hospital Schloss Werneck, Germany
1 Option
StudyID: 5aag660

## Slide 2: Background Total hip arthroplasty (THA)
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. | 1 THA: total hip arthroplasty
Gold-Standard procedure to plan THA1
X-ray image acquisition: Pelvis overview
      Lying or weight-bearing (optimal)
      Acquired in a.P. or including a second view lat.
Disadvantages
      Only indirect measurement of leg-length possible (true length only measurable with whole leg image)
      If additional CT acquisition is done (i.e., for 3D preoperative planning), patient is not in weight-bearing position
Measurements to plan THA (incl. resulting leg-length)
      Reference line within the pelvis, e.g., at the pelvic teardrop
      Parallel to the reference line, a second line is placed at the femoral bone, e.g., at the greater trochanter
      If the parallel line does not align with both reference points, the parallel difference is set equal to the leg-length discrepancy
1
2
3
1
2
3

## Slide 3: Clinical background
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. | 1 THA: total hip arthroplasty
Patient
Sex Female
Height 165 cm
BMI 25.7 kg/m²
Patient needed renewal implant of left hip to treat osteoarthritis.
After a previous THA1 implantation on the right, the cemented prosthesis caused increasing complaints during rehabilitation with hip misalignment and gait instability.
Hip overview imaging showed signs of loosening on right implant, which needs to be replaced after the treatment of the right side.
Anamnesis
StudyID: 5aag662
Year of birth 1964

## Slide 4: Clinical background
39 mm
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. | 1 THA: total hip arthroplasty
Patient
StudyID: 5aag662
Patient needed renewal implant of left hip to treat osteoarthritis.
After a previous THA1 implantation on the right, the cemented prosthesis caused increasing complaints during rehabilitation with hip misalignment and gait instability.
Hip overview imaging showed signs of loosening on right implant, which needs to be replaced after the treatment of the right side.
Leg-length measurement showed a leg-length discrepancy of 39 mm, but the cause (muscular vs. anatomical) remains questionable.
Anamnesis
Sex Female
Height 165 cm
BMI 25.7 kg/m²
Year of birth 1964

## Slide 5: Clinical background and indication for Multitom Rax True2scale Body Scan1
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. | 1 THA: total hip arthroplasty
Patient
Patient needed renewal implant of left hip to treat osteoarthritis.
After a previous THA1 implantation on the right, the cemented prosthesis caused increasing complaints during rehabilitation with hip misalignment and gait instability.
Hip overview imaging showed signs of loosening on right implant, which needs to be replaced after the treatment of the right side.
Leg-length measurement showed a leg-length discrepancy of 39 mm, but the cause (muscular vs. anatomical) remains questionable.
Indication for True2scale Body Scan1 Exact measurement of whole leg-length to understand the cause of leg-length discrepancy.
Anamnesis
Sex Female
Height 165 cm
BMI 25.7 kg/m²
Year of birth 1964

## Slide 6: Multitom Rax True2scale Body Scan1 Differences Pelvis Overview vs. T2S1
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. | 1 Option
Gold-standard
Pelvis overview
39 mm
Leg-length discrepancy | 39 mm
Tube voltage | 80.9 kV
Current time product | 38.0 mAs
Dose area product | 136.6 µGym²
StudyID: 5aag662
Leg-length discrepancy | 25 mm
Scan range | 97.8 cm
Scan time | 12.3 sec
Tube voltage | 80.7 kV
Current time product | 444.7 mAs
Dose area product | 86.3 µGym²
True2scale Body Scan1
a.p. using upright L protocol
25 mm
Pad of 1.5 cm (below right foot)
StudyID: 5aag661

## Slide 7: Multitom Rax True2scale Body Scan1 Diagnostic Findings & Results
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. | 1 Option
Results
StudyID: 5aag660
StudyID: 5aag661
Post-surgery
Pre-surgery
Pad of 1.5 cm (below right foot)
True2scale Body Scan1 revealed a 25 mm leg-length discrepancy
      Confirmed anatomical leg-length discrepancy
      Revision surgery
Follow-up scan after revision
Residual leg-length discrepancy of 10 mm with increasing subsidence/loosening of the right hip
      Planning of revision surgery on the right side

## Slide 8
1 The statements by Siemens Healthineers customers described herein are based on results that were achieved in the customer’s unique setting. Since there is no “typical” hospital and many variables exist (e.g., hospital size, case mix, level of IT adoption) there can be no guarantee that other customers will achieve the same results.
“The T2S scan makes it possible to objectify the patient’s subjective sensations and to reliably confirm or rule out diagnoses.”1
Manuel Scholl, MD Orthopedic Hospital Schloss Werneck, Germany

## Slide 9
The products/features (mentioned herein) are not commercially available in all countries. Their future availability cannot be guaranteed. True2scale Body Scan is an option.
Results from case studies are not predictive of results in other cases. Results in other cases may vary.
Manuel Scholl is employed by an institution that receives financial support from Siemens Healthineers for collaborations.